## Slide 1: Simultaneous addr+data (sad) testbench for HIBI v.3
Lasse Lehtonen, Erno Salminen
Tampere University of Technology
October 2011

## Slide 2: Overview
Allows testing new features that were added to version 3 of HIBI
  Addr transmittedsimultaneously with data (sad)
  New commands, e.g. exclusive access
  Supports HIBI interface revisions r3 and r4
Tests are written in SystemC (abbreviated sc)
HIBI is implemented in VHDL
Mixed-language simulation needs Modelsim SE version
Compile everything with script compile.sh
  It will print out the appropriate simulation command

## Slide 3: Structure
sc_main()
TopLevel topLevel(…)
Stimuli stimuli(…)
hibiv3_r3 (or hibiv3_r4)
wrapper_r*
wrapper_r*
…
wrapper_r*
wrapper_r*
…
…
agent
agent
…
bridge
bridge
sender
receiver
queue pkt_out
multimap pkt_in
packet
packet
…
packet
packet
…
thread
// Calls agents.
// All sent data is listed here.
sc module
VHDL
Legend:
SC_THREAD
(**)
(**) = R3 has threads and queues also for messages (hi-prior data)
constants.hh
// Defines data_width, #agents, addresses etc.
sc function()

## Slide 4: Summary
Test input is manually written into file stimuli.hh
  Rather simple way to test HIBI
  Loops are supported
Currently (2011-09-07), there are about 50k transfers
Testbench is rather ready at the moment