## Slide 1: HIBI_PE_DMA
ver. 1.00
author: Ari Kulmala
documentation: Juha Arvio
Modified: Lasse Lehtonen
Last modification: 01.02.2012

## Slide 2: Structure and configuration

## Slide 3: HIBI PE DMA block diagram
PE (Processing Element)
HIBI PE DMA
Dualport
RAM
HIBI wrapper
PE memory port
Memory write, read
DPRAM ports
DMA configuration interface
DMA configuration interface
DMA configuration registers
HIBI IP interface
DMA configuration parameters
Avalon master
Avalon master
Avalon slave
Avalon slave
Avalon slave
Avalon master
Avalon master
HIBI Tx
HIBI Rx
HIBI Tx
HIBI Rx

## Slide 4: HIBI PE DMA block diagram
PE (Processing Element)
HIBI PE DMA
Dualport
RAM
HIBI wrapper
PE memory port
DMA memory port
DPRAM ports
DMA configuration interface
DMA configuration interface
DMA configuration registers
HIBI IP interface
DMA configuration parameters

## Slide 5: HIBI PE DMA – CPU memory port
CPU
HIBI PE DMA
Dualport
RAM
HIBI wrapper
TTA port | Nios II port | width | direction | meaning
Dmem_data_in | D_readdata | 32 | Mem to CPU | Data from memory
- | D_waitrequest | 1 | Mem to CPU | Memory not ready, must wait
Dmem_data_out | D_writedata | 32 | CPU to mem | Data to memory
Dmem_addr | D_address | param | CPU to mem | Memory address
Dmem_mem_en | - | 1 | CPU to mem | Memory enable
Dmem_wr_en | - | 1 | CPU to mem | Write/read enable (1=wr, 0=rd)
- | D_read | 1 | CPU to mem | Read enable
- | D_write | 1 | CPU to mem | Write enable
Dmem_wr_mask | D_byteenable | 4 | CPU to mem | Byte enable for writes

## Slide 6: HIBI PE DMA – DMA memory port
CPU
HIBI PE DMA
Dualport
RAM
HIBI wrapper
DMA port | width | direction | meaning
Avalon_addr_out_rx | Param | DMA to mem | Receivers address to memory
Avalon_we_out_rx | 1 | DMA to mem | Receivers write enable
Avalon_be_out_rx | 4 | DMA to mem | Receivers byte enable for writes
Avalon_writedata_out_rx | 32 | DMA to mem | Receivers data to memory
Avalon_waitrequest_in_rx | 1 | Mem to DMA | Memory not ready, must wait
Avalon_addr_out_tx | Param | DMA to mem | Transmitters address to memory
Avalon_re_out_tx | 1 | DMA to mem | Transmitters read enable
Avalon_readdata_in_tx | 32 | Mem to DMA | Data from memory to transmitter
Avalon_waitrequest_in_tx | 1 | Mem to DMA | Memory not ready, must wait
Avalon_readdatavalid_in_tx | 1 | Mem to DMA | Data is valid on the data port

## Slide 7: HIBI PE DMA – DMA configuration interface
CPU
HIBI PE DMA
Dualport
RAM
HIBI wrapper
TTA port | Nios II port | DMA port | width | direction | meaning
Dmem_addr | D_address | Avalon_cfg_addr_in | Param | CPU to DMA | Memory address
Dmem_data_out | D_writedata | Avalon_cfg_writedata_in | 32 | CPU to DMA | Data to DMA config
Dmem_wr_en | D_write | Avalon_cfg_we_in | 1 | CPU to DMA | Write enable signal
Dmem_hibi_cfg_data_in | D_readdata | Avalon_cfg_readdata_out | 32 | DMA to CPU | Data from DMA to
Not( dmem_wr_en) | D_read | Avalon_cfg_re_in | 1 | CPU to DMA | Read enable signal (inverted write enable on TTA)
Dmem_hibi_cfg_en | - | Avalon_cfg_cs_in | 1 | CPU to DMA | Configuration enable signal (created by Avalon on Nios II)

## Slide 8: HIBI PE DMA – DMA configuration registers
CPU
HIBI PE DMA
Dualport
RAM
HIBI wrapper
Register | Width | Offset from base address | R/W (access right) | meaning
Rx chan0: data buffer address | 32 | 0 | CPU: RW DMA: R | Rx channel 0: data buffer address (in dpram)
Rx chan0: hibi address | 32 | 1 | CPU: RW DMA: R | Rx channel 0: hibi address
Rx chan0: data amount | 16 | 2 | CPU: RW DMA: R | Amount of data to be received
Rx chan0: current address pointer | 32 | 3 | CPU: R DMA: RW | DMAs current address to dpram
Status and configuration register | 32 | 4 | CPU: RW DMA: RW | Status register is upper 16 bits, configuration register is lower 16 bits
Rx channels init register | 32 | 5 | CPU: RW DMA: R | Tells whether a channel is initialized.
Rx chan0: words read by stream channel | 32 | 6 | CPU:R DMA:W | Tells how many words have been reseived
Rx IRQ register | 32 | 7 | CPU: RW DMA: RW | Receiver interrupt register

## Slide 9: HIBI PE DMA – DMA configuration registers
CPU
HIBI PE DMA
Dualport
RAM
HIBI wrapper
Register | Width | Offset from base address | R/W (access right) | meaning
Tx chan: data buffer address | 32 | 8 | CPU: RW DMA: R | Transmitter data buffer address (in dpram)
Tx chan: data amount | 16 | 9 | CPU: RW DMA: R | Amount of data to be sent
Tx chan: command register | 32 | 10 | CPU: RW DMA: R | Command to be sent
Tx chan: Hibi address | 32 | 11 | CPU: RW DMA: R | Receivers hibi address
Current address on Hibi rx interface | 32 | 12 | CPU:R DMA:W | Shows the address on Hibi rx interface
- | 32 | 13-15 | - | not in use
Rx chan1: data buffer address | 32 | 16 | CPU: RW DMA: R | Rx channel 0: data buffer address (in dpram)
Rx chan1: hibi address | 32 | 17 | CPU: RW DMA: R | Rx channel 0: hibi address
Rx chan1: data amount | 16 | 18 | CPU: RW DMA: R | Amount of data to be received
Rx chan1: current address pointer | 32 | 19 | CPU: R DMA: RW | DMAs current address to dpram
... | ... | ... | ... | ...

## Slide 10: HIBI PE DMA – DMA configuration registers
Rx channel register address offset in general
  X is the index of channel
CPU
HIBI PE DMA
Dualport
RAM
HIBI wrapper
Register | Formula for address offset from base address
Rx chanX: data buffer address | X*16
Rx chanX: hibi address | X*16+1
Rx chanX: data amount | X*16+2
Rx chanX: current address pointer | X*16+3
Rx chanX: received words for stream channel | X*16+6

## Slide 11: HIBI PE DMA internal
DMA configuration and status registers
Tx
Processing element
Rx
Rx
Rx
Dualport RAM
HIBI IP interface
Ctrl
Tx
Rx
Optional direct path

## Slide 12: HIBI PE DMA configuration parameters
Generic and VHDL default | Category | Category | Type | Value range | Description
data_width_g : integer := 32 | Structural | Bus widths | Bits | 32 or 64 | Width of data
addr_width_g : integer := 32 | Structural | Bus widths | Bits | dpram_addr_width <= x <= data_width_g | Address width
amount_width_g : integer := 16 | Structural | Bus widths | Bits | 1 to data_width_g | Maximum bit width of data amount value
n_chans_g : integer := 8 | Structural | Channels | Number | 1 to N | Number of Rx channels in HIBI DMA PE
n_chans_bits_g : integer := 3 | Structural | Bus widths | Bits | Ceil(log2(n_chans_g)) | Number of bits needed to present all the Rx channels
hibi_address_cmp_lo_g : integer := 0 | Structural | Bus widths | Number | Less than hibi_addr_cmp_hi_g | Least significant bit of a hibi address
hibi_addr_cmp_hi_g : integer := 27 | Structural | Bus widths | Number | More than hibi_addr_cmp_lo_g | Most significant bit of a hibi address

## Slide 13: Functionality

## Slide 14: HIBI_PE_DMA component
An DMA controller to interface processor with Hibi
  Originally for Nios
DMA copies data to/from dual-port memory from/to HIBI
Nios
dual-port RAM
(on-chip)
HIBI_PE_DMA
(DMA)
HIBI wrapper
HIBI bus
instr.memory
(on/off-chip)

## Slide 15: Sending data to HIBI
CPU has the data ready in memory
  e.g. result of DCT
CPU configures DMA
DMA sends the data to the given address as fast as possible, 1 word/cycle in optimal case
Nios
dual-port RAM
(on-chip)
HIBI_PE_DMA
HIBI wrapper
HIBI bus
instr.memory
(on/off-chip)
1
2
3
Fig. Send data to HIBI

## Slide 16: Receiving data from HIBI
CPU configures DMA
DMA copies the incoming data to DPRAM
DMA interrupts CPU when a predefined number of words have been received
CPU knows that data is ready in memory and uses it
DMA can wait for many incoming transfers at the same time.
Nios
dual-port RAM
(on-chip)
HIBI_PE_DMA
HIBI wrapper
HIBI bus
instr.memory
(on/off-chip)
4
1
2
3
Fig. Receive data from HIBI

## Slide 17: Receiving unknown data from HIBI
CPU doesn’t configure DMA
DMA receives address that doesn’t match any channel
DMA interrupts CPU
CPU reads incoming transfer’s address and configures a channel for it
DMA writes transfer to DPRAM
DMA interrupts CPU when transfer is ready
CPU reads the data
Nios
dual-port RAM
(on-chip)
HIBI_PE_DMA
HIBI wrapper
HIBI bus
instr.memory
(on/off-chip)
4
2
3
5
6
7
1

## Slide 18: Interfaces
Nios is master component in Avalon switching fabric (’Avalon bus’), dubbed AM in fig
HIBI_PE_DMA is both
  Avalon master, AM, for accessing DPRAM
  Avalon slave, AS, for getting the configuration from CPU and interrupting it upon completion
DP-RAM acts as Avalon slave (both ports)
Nios
dual-port
RAM
HIBI_PE_DMA
HIBI wrapper
HIBI bus
instr.memory
(on/off-chip)
Fig. Receive data from HIBI
AS
AM
AS
AS
AM

## Slide 19: Software interface of the HIBI_PE_DMA
HIBI_PE_DMA has a set of memory-mapped registers, e.g.
  TX+RX: amount, mem_addr, hibi_addr
    TX only: command to send
  Common: control, status, irq_chan
Software routines are located in directory drv
There are two types of accesses
  Low-level macros
  Higher-level functions

## Slide 20: Accessing HIBI_PE_DMA from software
Registers can be directly accessed with low-level macros one at a time
  e.g. macro HPD_TX_AMOUNT(...) sets the amount register for outgoing transfer
Higher-level functions utilize these macros
  e.g. HIBI_TX(...)
    checks that previous send operation is complete
    calls hpd_send
      runs macros HPD_TX_ADDR, TX_AMOUNT, HIBI_ADDR, TX_COMM, and TX_START
    releases the tx channel
Highest-level functions need eCos operating system
  Ipc_tx(...) can do e.g. (de)fragmentation of large transfers

## Slide 21: Functional model
Following example assumes the system below
A data transfer between two Nios2 cpus
Nios2_cpu0
HIBI_PE_DMA_buf0
(=DPRAM)
HIBI_PE_DMA_0
HIBI wrapper
HIBI bus
instr.memory
(on/off-chip)
Nios2_cpu1
HIBI_PE_DMA_buf1
(=DPRAM)
HIBI_PE_DMA_1
HIBI wrapper
instr.memory
(on/off-chip)
hibi

## Slide 22: Functional model (2)
can be divided into 12 parts:
Cpu0 writes the data memory that the HIBI_PE_DMA_0 component can access (internal ram block). Data blocks starts from address TX_ADDRESS on Avalon
Cpu1 sets the HIBI_PE_DMA_1 to receive TX_LENGTH 32-bit words from HIBI, data will be written avalon address RX_ADDRESS (internal ram block), data is assumed to arrive to HIBI_ADDRESS
Cpu0 sets HIBI_PE_DMA_0 to send TX_LENGTH 32-bit words to HIBI_ADDRESS (addr of Cpu1 in HIBI)
HIBI_PE_DMA_0 starts reading data from TX_ADDRESS
HIBI_PE_DMA_0 gets the data
HIBI_PE_DMA_0 writes the data to Hibi
HIBI_PE_DMA_1 gets the data from Hibi and identifies it based on its address
HIBI_PE_DMA_1 writes the data to RX_ADDRESS
HIBI_PE_DMA_1 sends an interrupt signal to Cpu1
Cpu1 clears the interrupt signal
Cpu1 starts reading transmit data from RX_ADDRESS
Cpu1 gets the data
I. Init tx and rx info to DMAs
II. DMAs running
III. Clear the rx DMA

## Slide 23: Functional model
HIBI_PE_DMA_buf_0
Nios2_cpu0
Nios2_cpu1
HIBI_PE_DMA_buf_1
HIBI_PE_DMA_1
HIBI_PE_DMA_0
hibi
tx_data
5:
set transmit TX_LENGTH words to HIBI_PE_DMA_1
set transmit address on avalon
3:
tx_data
1:
set receive TX_LENGTH words from HIBI_PE_DMA_0
set receive address on avalon
2:
read from
receive address
11:
clear interrupt
10:
tx_data
12:
tx_data
8:
interrupt TX_LENGTH words received
9:
read from
transmit address
4:
tx_data
6:
tx_data
7: