## Slide 1: N2H2: Nios to Hibi rev. 2
ver. 1.00
author: Ari Kulmala
documentation: Juha Arvio
Modified: Lasse Lehtonen
Last modification: 08.03.2011

## Slide 2: N2H2 component
An DMA controller to interface processor with Hibi
  Originally for Nios, hence the name Nios-to-HIBI v2 = N2H2
DMA copies data to/from dual-port memory from/to HIBI
Nios
dual-port RAM
(on-chip)
N2H2
(DMA)
HIBI wrapper
HIBI bus
instr.memory
(on/off-chip)

## Slide 3: Sending data to HIBI
CPU has the data ready in memory
  e.g. result of DCT
CPU configures DMA
DMA sends the data to the given address as fast as possible, 1 word/cycle in optimal case
Nios
dual-port RAM
(on-chip)
N2H2
HIBI wrapper
HIBI bus
instr.memory
(on/off-chip)
1
2
3
Fig. Send data to HIBI

## Slide 4: Receiving data from HIBI
CPU configures DMA
DMA copies the incoming data to DPRAM
DMA interrupts CPU when a predefined number of words have been received
CPU knows that data is ready in memory and uses it
DMA can wait for many incoming transfers at the same time.
Nios
dual-port RAM
(on-chip)
N2H2
HIBI wrapper
HIBI bus
instr.memory
(on/off-chip)
4
1
2
3
Fig. Receive data from HIBI

## Slide 5: Receiving unknown data from HIBI
CPU doesn’t configure DMA
DMA receives address that doesn’t match any channel
DMA interrupts CPU
CPU reads incoming transfer’s address and configures a channel for it
DMA writes transfer to DPRAM
DMA interrupts CPU when transfer is ready
CPU reads the data
Nios
dual-port RAM
(on-chip)
N2H2
HIBI wrapper
HIBI bus
instr.memory
(on/off-chip)
4
2
3
5
6
7
1

## Slide 6: Interfaces
Nios is master component in Avalon switching fabric (’Avalon bus’), dubbed AM in fig
N2H2 is both
  Avalon master, AM, for accessing DPRAM
  Avalon slave, AS, for getting the configuration from CPU and interrupting it upon completion
DP-RAM acts as Avalon slave (both ports)
Nios
dual-port
RAM
N2H2
HIBI wrapper
HIBI bus
instr.memory
(on/off-chip)
Fig. Receive data from HIBI
AS
AM
AS
AS
AM

## Slide 7: Software interface of the N2H2
N2H2 has a set of memory-mapped registers, e.g.
  TX+RX: amount, mem_addr, hibi_addr
    TX only: command to send
  Common: control, status, irq_chan
Software routines are located in directory drv
There are two types of accesses
  Low-level macros
  Higher-level functions

## Slide 8: Accessing N2H2 from software
Registers can be directly accessed with low-level macros one at a time
  e.g. macro N2H_TX_AMOUNT(...) sets the amount register for outgoing transfer
Higher-level functions utilize these macros
  e.g. HIBI_TX(...)
    checks that previous send operation is complete
    calls N2H_send
      runs macros N2H_TX_ADDR, TX_AMOUNT, HIBI_ADDR, TX_COMM, and TX_START
    releases the tx channel
Highest-level functions need eCos operating system
  Ipc_tx(...) can do e.g. (de)fragmentation of large transfers

## Slide 9: Functional model
Following example assumes the system below
A data transfer between two Nios2 cpus
Nios2_cpu0
n2h2_buf0
(=DPRAM)
n2h2_0
HIBI wrapper
HIBI bus
instr.memory
(on/off-chip)
Nios2_cpu1
n2h2_buf1
(=DPRAM)
n2h2_1
HIBI wrapper
instr.memory
(on/off-chip)
hibi

## Slide 10: Functional model (2)
can be divided into 12 parts:
Cpu0 writes the data memory that the N2H2_0 component can access (internal ram block). Data blocks starts from address TX_ADDRESS on Avalon
Cpu1 sets the N2H2_1 to receive TX_LENGTH 32-bit words from HIBI, data will be written avalon address RX_ADDRESS (internal ram block), data is assumed to arrive to HIBI_ADDRESS
Cpu0 sets N2H2_0 to send TX_LENGTH 32-bit words to HIBI_ADDRESS (addr of Cpu1 in HIBI)
N2H2_0 starts reading data from TX_ADDRESS
N2H2_0 gets the data
N2H2_0 writes the data to Hibi
N2H2_1 gets the data from Hibi and identifies it based on its address
N2H2_1 writes the data to RX_ADDRESS
N2H2_1 sends an interrupt signal to Cpu1
Cpu1 clears the interrupt signal
Cpu1 starts reading transmit data from RX_ADDRESS
Cpu1 gets the data
I. Init tx and rx info to DMAs
II. DMAs running
III. Clear the rx DMA

## Slide 11: Functional model
n2h2_buf_0
Nios2_cpu0
Nios2_cpu1
n2h2_buf_1
n2h2_1
n2h2_0
hibi
tx_data
5:
set transmit TX_LENGTH words to n2h2_1
set transmit address on avalon
3:
tx_data
1:
set receive TX_LENGTH words from n2h2_0
set receive address on avalon
2:
read from
receive address
11:
clear interrupt
10:
tx_data
12:
tx_data
8:
interrupt TX_LENGTH words received
9:
read from
transmit address
4:
tx_data
6:
tx_data
7: