## Slide 1
Author | Version | Project | Date | Changes
Antti Kojo | v1 | FunBase | 2009-06-29 | 
Antti Alhonen | v1.1 |  | 2012-01-22 | Ported to work with 16-bit sdram (DE2). Hibiv3 update.
Document history
SDRAM controller

## Slide 2
SDRAM controller
Register(s) | Address | Size
Read request | HIBI base address | 1
Write request | HIBI base address + 1 | 1
Read configure | HIBI base address + 2 | num_of_read_ports_g
Write configure | HIBI base address + 2 + num_of_read_ports_g | num_of_write_ports_g
SDRAM controller enables read and write access to external SDRAM memory through HIBI interconnection network
Uses HIBI interconnection network v3
Uses platform specific interface to access the actual memory; select either:
  sdram_controller_de2.vhd and sdram_toplevel_de2.vhd or
  sdram_controller_stratix.vhd and sdram_toplevel_stratix.vhd
Location in SVN:
  /trunk/ip.hwp.storage/hibi_sdram/
Register map

## Slide 3
Operation (External)
Read operation configuration words:
SDRAM source address
Word count
Target HIBI address for data
RowCountAndStride (Used when reading rectangular areas from memory, use zero for linear read operation)
Read operation:
Request read permission by sending your HIBI address to read request register
SDRAM-controller replies with offset value (permission granted if offset differs from zero)
Calculate read configuration register address (Add offset to SDRAM controller base HIBI address)
Write configuration words to configuration register
Read operation starts after 4th configuration word is written to register
Write operation configuration words:
SDRAM target address
Word count
RowCountAndStride (Used when writing rectangular areas to memory, use zero for linear write operation)
Read operation:
Request write permission by sending your HIBI address to write request register
SDRAM-controller replies with offset value (permission granted if offset differs from zero)
Calculate write configuration register address (Add offset to SDRAM controller base HIBI address)
Write configuration words to configuration register
Start writing data to configuration register after 3rd configuration word is written to register

## Slide 4
Example of read sequence
SDRAM-read
SDRAM-read
interaction
[
]
: SDRAM-controller
: NIOS2HIBI
: NIOS II
[Control register
address offset != 0]
Wait for NIOS2HIBI interrupt
loop
Configuration register HIBI address =
SDRAM controller base HIBI address +
control register address offset
Configuration words:
- SDRAM source address
- Word count
- Data target HIBI address
- rowCountAndStride
Control register address offset
6:
Transfer data from SDRAM
14:
return
2:
return
4:
Send configured HIBI channel address of NIOS II
to SDRAM controller read permission request HIBI address
5:
NIOS2HIBI interrupt
7:
return
12:
Send configuration words to SDRAM controller
configuration register HIBI address
13:
NIOS2HIBI interrupts when read is done
15:
return
10:
Configure receiving HIBI channel
to listen specified HIBI address
1:
Send configured HIBI channel address to SDRAM controller
3:
Calculate SDRAM controller configuration
register HIBI address
8:
Send configuration words to SDRAM controller
configuration register HIBI address
11:
Configure receiving HIBI channel to listen
specified HIBI address for data
9:

## Slide 5
Example of write sequence
SDRAM-write
SDRAM-write
interaction
[
]
: SDRAM-controller
: NIOS2HIBI
: NIOS II
[Control register
address offset != 0]
Wait for NIOS2HIBI interrupt
loop
Configuration register HIBI address =
SDRAM base HIBI address +
control register address offset
Configuration words:
- SDRAM target address
- Word count
- rowCountAndStride
Control register address offset
6:
return
2:
return
4:
Send configured HIBI channel address of NIOS II
to SDRAM controller write permission request address
5:
NIOS2HIBI interrupt
7:
return
10:
Send configuration words to SDRAM
controller configuration register HIBI address
11:
return
13:
NIOS2HIBI interrupts when write is done
15:
Write to SDRAM
14:
Configure receiving HIBI channel
to listen specified HIBI address
1:
Send configured HIBI channel address to SDRAM controller
3:
Calculate SDRAM controller configuration
register HIBI address
8:
Send configuration words to SDRAM
controller configuration register HIBI address
9:
Start writing data to SDRAM
controller configuration register
12: