## Slide 1
Author | Version | Project | Date
Antti Kojo | v1 | FunBase | 2009-07-02
Document history
eCos SDRAM driver

## Slide 2
eCos SDRAM driver
Implements API to read, write and configure SDRAM controller through HIBI
Depends on:
  HIBI/IPC eCos driver
  eCos (semaphores)
Application using this driver has to implement callback-function, which is used for data receiving from SDRAM controller.

## Slide 3
SDRAM driver API
Fuction prototype | Description
void sdram_init(); | Driver initialization function. Reserves N2H channels and initializes a semaphore.
bool sdram_write ( uint32* const src, const uint32 sdram_addr, const uint32 words ); | Writes data to SDRAM. Parameters src: Pointer to source data sdram_addr: SDRAM target address for write operation words: Amount of data words to write
void sdram_read ( const uint32 sdram_addr, const uint32 words ); | Reads data from SDRAM. Parameters sdram_addr: SDRAM source address for read operation words: Amount of data words to read
extern void sdram_rx_end (uint32* data, uint32 data_length); | User application must implement this function. Function is called after data has been received from SDRAM. Parameters data: Pointer to data received from SDRAM. data_length: Amount of received data in bytes.

## Slide 4
Fuction prototype | Description
uint32 sdram_config (const uint32 sdram_byte_addr, const uint32 words, const uint8 operation, const uint32 read_chn_addr, const uint32 row_count_and_stride); | Configure SDRAM controller for read/write operations. Parameters sdram_byte_addr: SDRAM byte address for read and write operations words: Amount of words to read/write operation: Use parameter SDRAM_WRITE_OPERATION when writing and SDRAM_READ_OPERATION when reading. read_chn_addr: In case of read operation, data from SDRAM will be written to this hibi address. In case of write operation, this parameter is not used. row_count_and_stride: This parameter is used when reading/writing rectangular memory areas. Use zero for linear operations. Return In case of write operation, this function returns HIBI address where the data should be written.