## Slide 1: HIBI_PE_DMA Example

## Slide 2: HIBI bus operation

## Slide 3: HIBI burst transfer (streaming)
A burst transfer consist of bus command and destination address followed by data (one or more data words)
Sending IP is responsible of setting all these
Sender address is not transmitted
  receiver does not know where data is coming from
  sender information must be included in data payload OR agreed at design time which IP-blocks send data to which
HIBI wrapper
[HIBI bus command]
[Destination address]
[HIBI bus command]
[Data]
HIBI wrapper
Rx FIFO
Tx FIFO
IP block
IP
IP block
IP
…

## Slide 4: HIBI random access transfer (normal transfer)
Normal transfer consist of bus command, destination address and data sent in parallel every clock cycle
Sending IP is responsible of setting all these
Sender address is not transmitted
  receiver does not know where data is coming from
  sender information included in data payload OR agreed at design time which IP-blocks exchange data
HIBI wrapper
HIBI wrapper
Rx FIFO
Tx FIFO
IP block
IP
IP block
IP
[HIBI bus command]
[Destination address]
[Data]
[HIBI bus command]
[destination address]
[Data]
…

## Slide 5: HIBI addresses
All wrappers have unique addresses in HIBI bus address space
IP block address space is transparent (same as HIBI address space) or opaque (independent)
HIBI wrapper
HIBI transmission
HIBI wrapper
IP block
Registers for configuration
Offset(s) +
[IP-block base address]
Registers
for IP-block
Offset(s) +
[IP-block base address]
IP-block registers and memory locations
e.g. 0x00000 -
0xfffff
HIBI transmission
IP’s local address space
HIBI address space

## Slide 6: HIBI channel
This is used in a HIBI_PE_DMA controller, not in normal HIBI wrapper
HIBI channel is an address in HIBI address space through which data is transmitted
Rx buffers are organized as channels
  Only memory space limits how many buffers (channels) exists at the same time
Channels have implicit meanings that must be agreed
  Who (what IP-block or CPU) sends data to which channel, since otherwise the sender is not known (HIBI does not send sender ID in transfers)
  Possible explicit meaning of channel like ”DCT transform Q-parameter”
HIBI wrapper
HIBI transmission
HIBI wrapper / HIBI PE DMA
IP block
[IP-block base address K] + 1
0x00100 -
0x00110
HIBI transmission
[IP-block base address K] + 2
[IP-block base address K] + 3
HIBI transmission
Channel 1
Channel 2
Channel 3
0x00002 -
0x000ff
0x00001
[IP-block base address L ]
[IP-block base address N ]
Register A
Buffer A
Buffer B
IP’s local address space
HIBI address space

## Slide 7: Example
Following example assumes the system below
A data transfer between two IP-blocks (CPUs)
Data buffering takes place in dual-port RAM that both CPU and DMA controller can access at the same time
cpu0
dma_buf_0
(=DPRAM)
hibi_pe_
dma_0
HIBI wrapper
HIBI bus
instr.memory
(on/off-chip)
cpu1
dma_buf_1
(=DPRAM)
hibi_pe_
dma_1
HIBI wrapper
instr.memory
(on/off-chip)
HIBI segment

## Slide 8: Sending a packet (fixed size transfer)
CPU reserves buffer space from dual-port memory
CPU copies/writes data to dual-port memory
CPU configures DMA transfer
  Size of transfer and destination IP-block’s HIBI address (not the local CPU address)
DMA reads data from dual-port memory and sends the data to the configured HIBI address
CPU
Dual-port
RAM
HIBI PE
DMA
HIBI wrapper
HIBI bus
instr.memory
(on/off-chip)
1
2
3
Data memory
(on/off-chip)
1
CPU’s local address space
Global (HIBI) address space not accessible directly by CPU programs

## Slide 9: Receiving a packet (fixed size transfer)
CPU reserves buffer space from dual-port memory
CPU configures DMA
  Size of transfer and HIBI address in which data is received
DMA copies the incoming data to DPRAM
DMA interrupts CPU when a configured number of words have been received
CPU knows that data is ready in dual-port memory and uses it/copies to its data memory
(DMA can wait for many incoming transfers at the same time)
CPU
dual-port
RAM
HIBI PE
DMA
HIBI wrapper
HIBI bus
instr.memory
(on/off-chip)
5
2
3
4
Data memory
(on/off-chip)
5
CPU’s local address space
Global (HIBI) address space not accessible directly by CPU programs

## Slide 10: Receiving ad-hoc data
CPU has not yet configured any DMA transfers
DMA receives address that doesn’t match any channel
DMA interrupts CPU
CPU reads interrupt causeand incoming transfer’s address. Reserves buffer and configures a new channel for it
DMA writes transfer to buffer
DMA interrupts CPU when transfer is ready
CPU reads the data
Nios
dual-port RAM
(on-chip)
HIBI_
PE_DMA
HIBI wrapper
HIBI bus
instr.memory
(on/off-chip)
4
2
3
5
6
7
1

## Slide 11: Receiving streaming data (continuous, no packet borders)
CPU reserves buffer space from dual-port memory
CPU configures DMA
  Size of transfer and HIBI address in which data is received
DMA copies the incoming data to DPRAM
DMA interrupts CPU when buffer gets full or when incoming data stream stops
CPU reads whole buffer and acknowledges to DMA
Streaming continues as in 3.
CPU
dual-port
RAM
HIBI PE
DMA
HIBI wrapper
HIBI bus
instr.memory
(on/off-chip)
5
2
3
4
Data memory
(on/off-chip)

## Slide 12: Notes about HIBI transfers
HIBI is a low-level transfer mechanism
SW side must know other IP-blocks’ HIBI addresses and HIBI bus commands to transfer data
Not reasonable for user applications to know these low-level details
We hide these details by SW platform macros and functions

## Slide 13: Hardware dependent SW

## Slide 14: SW platform for NIOS and uC/OS-II RTOS
HIBI_PE_DMA controller
Dualport
On-chip RAM
NIOS processor
HW platform
SW platform
Application SW
Hardware abstraction
SW abstraction (API)

## Slide 15: Hardware dependent software
General term that refers to such SW that directly manipulates HW
HdSW belongs to HAL (Hardware Abstraction Layer)
Hardware platform topmost layer and SW platform lowest layer communication
Physical interrupt lines, registers and memory locations are accessed by HdSW
  Transmitting data
  Configuring

## Slide 16: Step by step from HW to SW
Physical structure of IP-blocks (at IP-block design time)
  Registers, interrupts, memory locations, special status and control signals
Generic values are fixed for each instantiated IP-block (at HW integration time)
  Base addresses, register widths, …
System specific SW configuration files are provided for the physical addresses (e.g. headers)
  Physical addresses are given names/symbols
Low-level macros are provided to handle the registers at word/bit level
  Add primitive behavior of handling the HW registers
  May add control and protection against lowest level protocol violations
  Basic operation is register read/write
Functions
  Hide the low-level register access
  Provide system independent but device specific protocol to send/receive/configure/get status
  Without operating system, these can be used directly from applications
OS dependent APIs
  HAL (hardware abstraction layer) API
  Standardized, system and device independent functions to access the device
  E.g. Unix char and block devices (fopen, fcose, …)
  Add control for interrupt services and mutual exclusion
OS independent APIs
  Standardized APIs, but do not depend on OS
  E.g. MCAPI, MPI, OpenCL

## Slide 17: Example SoC hardware
Two separate NIOS subsystems designed with SoPC builder
NIOS subsystems and HIBI network instantantiated in Quartus
cpu0
dma_buf_0
(=DPRAM)
hibi_pe_
dma_0
HIBI wrapper
HIBI bus
instr.memory
(on/off-chip)
cpu1
dma_buf_1
(=DPRAM)
hibi_pe_
dma_1
HIBI wrapper
instr.memory
(on/off-chip)
HIBI segment
nios_2x_soc.vhd
hibi_2x_r4_segment.vhd
nios_sram_subsystem.vhd
nios_sdram_subsystem.vhd

## Slide 18: 1. Hardware generics (VHDL)
HW implementation time generics that can not be changed at run time
Word length, address range (on HIBI addr space)
Channel
  Seen from HIBI, each channel have own HIBI address to receive data from other IP-blocks
  Seen from CPU, each channel is a buffer in dual port memory
Bits for words_width_g tells the maximum packet size in a buffer, e.g. 8 bits means max 256 words in the buffer
CPU
Dualport
RAM
HIBI PE DMA
HIBI wrapper
CPU MEMORY

## Slide 19: 2. Registers (VHDL)
Note: number of implemented registers depends on generics (n channels means 5n + 8 registers in total)
Register addresses are in CPUs address space (not HIBI)
Purpose: Initialization, DMA configuration, status, transfer control for CPU, transfer control for HIBI bus
CPU
Dualport
RAM
HIBI PE DMA
HIBI wrapper
CPU MEMORY

## Slide 20: 3. System and instance specific values (VHDL)
NIOS subsystem address space
  SoPC builder project stores address information (.sopc XML file)
  Altera tools automatically generate system.h for SW
HIBI address space
  Project file .bdf (if defined in Quartus) OR the top-level VHDL file including all wrappers
  User must manually write .h for SW (Kactus2 will do this automatically in the future versions)
CPU
Dualport
RAM
HIBI PE DMA
HIBI wrapper
CPU MEMORY

## Slide 21: HW file dependencies (VHDL)
Note: this is not complete, just example
Criteria for modules and dependencies: think how to use layers to help reuse and portability
File | Dependency | Description / what defined
nios_2x_soc.vhd |  | Top level VHDL for the complete system (2 NIOS subsystems and HIBI bus
hibi_2x_r4_segment.vhd |  | Instantiates and connects HIBI wrappers. Defines physical system specific HIBI addresses
nios_sram_subsystem.vhd |  | Generated in SoPC and instantiates NIOS, HIBI PE DMA, local mem and peripherals
hibi_pe_dma.vhd |  | DMA component top VHDL
hpd_tx_control.vhd |  | Transmission control module
hpd_rx_and_conf.vhd |  | Reception and general control module
hpd_rx_stream_chan.vhd |  | Streaming transfer cahnnel module
hpd_rx_packet_chan.vhd |  | Receiver component for known packet size
hibi_pe_dma_hw.tcl | ./hpd_rx_channel.vhd ./hpd_rx_and_conf.vhd ./hibi_pe_dma.vhd ./hpd_rx_stream.vhd | Creates a SoPC/QSys component that has 2x avalon master, 1x avalon slave, 1x IRQ out and 1x HIBI R1 IP side bus

## Slide 22: Typical SW layers
HW platform
SW platform
Application SW
Hardware abstraction
SW abstraction (API)
HIBI addresses:
all HIBI wrappers
NIOS sram subsystem addresses:
HIBI_PE_DMA registers,
Local memory, etc.
NIOS sdram subsystem addresses:
HIBI_PE_DMA registers,
Local memory, etc.
Macros to access registers
Functions to access specific devices
Standard device classes
Standard APIs
Applications

## Slide 23: 4. HW defining SW files
Both HIBI and NIOS subsystems have separate header files
Arrows show from where header gets its content
  Altera generates headers automatically, HIBI-related headers must be created manually (automatically if Kactus2 and IP-XACT generators are used)
Note: only examples, not complete listing of files
File | Depen-dency | Description / what defined | NIOS specific | HIBI specific | HPD specific
nios_2x_soc.vhd |  | VHDL file defining physical HIBI addresses | - | x | 
nios_2x_soc.h |  | Header file defining all system specific HIBI register and memory addresses | - | x | x
nios_1x_subsys.sopcinfo |  | Defines SoPC project specific addresses. Note in this example we have one NIOS per SoPC | x | - | -
system.h |  | Processor subsystem specific address definitions (SoPC generated defines for NIOS address spaces) | x | - | -
sys/alt_irq.h |  | Defines NIOS specific interrupt service routines | x | - | x

## Slide 24: 5. Macros
Macros for HIBI PE DMA
Expects physical addressess are named and defined in a header file
Note: only register access (R and W), not any protocol

## Slide 25: 6. Functions – Send (example)
Send data from dual-port memory buffer to another CPU via HIBI
Note: added low-level protocol, still includes HIBI-specific things like HIBI bus command

## Slide 26: Functions – Initilaize receive (example)
Initializes packet reception from HIBI to dual-port memory buffer

## Slide 27: Hardware abstraction layer
The HAL application programming interface (API) provides a standard (POSIX-like) interface to the hardware
HAL is also called BSP (Board Support Package)
The HAL provides a variety of generic device classes
  character-mode
  file subsystem
  Ethernet
  timestamp and system timers
  direct memory access (DMA)
  flash memory
Note: device sharing (exclusion) and execution control (e.g. interrupts) can be implemented on HAL or OS level

## Slide 28: 7. Drivers (for NIOS HAL)
Workflow overview:
Define registers
  system.h, <component_name>_regs.h
Write the driver code
  Typically uses macros and functions
  Decide polling/interrupting mode
  Decide mutual exclusion
  Decide blocking/non-blocking
Define device class (if standard)
Publish driver to NIOS HAL
  A TCL script specifying how to add the driver to NIOS
Register the driver
  Include to initialization code
Note: this is your task in execrsise 4!

## Slide 29: Standard device driver
Task: implement the character device functions in your driver (open, close etc.)
Example: unix character mode device

## Slide 30: Notes about standard devices
No global address space
  NIOS sram
  NIOS sdram
  HIBI bus
To send data between NIOSes (or any HIBI IP-blocks) we must make global agreement of identification (e.g. names of devices to refer to)
  Must use same header files for this on all processor SW projects
Standard devices are at moderate low abstraction level and help abstracting the HW
Higher level APIs are required to make application e.g. OS indpenedent

## Slide 31: Summary (example, not complete)
File | Depen-dency | Description / what defined | NIOS specific | HIBI specific | HPD specific
nios_2x_soc.vhd |  | VHDL file defining physical HIBI addresses | - | x | 
nios_2x_soc.h |  | Header file defining all system specific HIBI register and memory addresses | - | x | x
nios_1x_subsys.sopc |  | Defines SoPC project specific addresses. Note in this example we have one NIOS per SoPC | x | - | -
system.h |  | Processor subsystem specific address definitions (SoPC generated defines for NIOS address spaces) | x | - | -
sys/alt_irq.h |  | Defines NIOS specific interrupt service routines | x | - | x
hpd_isr_fifo.h hpd_isr_fifo.c |  | Generic interrupt queue (FIFO) for saving interrupt information (what interrupted), header and implementation | - | - | -
hpd_macros.h |  | System independent macros for accessing HIBI_PE_DMA registers | - | x | x
hpd_functions.h hpd_functions.c |  | System independent functions for handling initialization, sending, receiving, interrupt handling | - | x | x
hpd_functions_nios.h hpd_functions_nios.c |  | NIOS specific functions, interrupt | x | x | x
hpd_dma_device_nios_hal.h hpd_dma_device_nios_hal.c |  | Standard DMA device on NIOS HAL | (x) | - | -
mcapi_transport_nios |  | Multicore association MCAPI API for applications | - | - | -
main_with_no_os.c |  | User application (without OS) | - | - | x
main_with_ucosii.c |  | User application (with uC/OS-II RTOS) | - | - | -