## Slide 1: Instructions to build HIBI_PE_DMA testing system (SOPC+NIOS II Eclipse)
Lasse Lehtonen
Last modification: 29.3.2011

## Slide 2: Intro
This document describes briefly how to build a SOPC and NIOS II Eclipse project to be used with the associated system level testbench and examples (..tb/system/*)

## Slide 3: Abbreviations
HPD = HIBI_PE_DMA

## Slide 4: Test system to be created
Nios
dual-port RAM
(on-chip)
HIBI_PE_DMA
(DMA)
HIBI wrapper
instr.memory
(on/off-chip)
Nios
dual-port RAM
(on-chip)
HIBI_PE_DMA
(DMA)
HIBI wrapper
HIBI bus
instr.memory
(on/off-chip)
Nios
dual-port RAM
(on-chip)
HIBI_PE_DMA
(DMA)
HIBI wrapper
instr.memory
(on/off-chip)

## Slide 5: Design flow
Used tools: Quartus, Sopc, eclipse, modelsim
Quartus: base for SOPC project
SOPC: define the HW platform
Modelsim: simulate the whole system
Eclipse: create SW platform

## Slide 6: Building SOPC project
Create Quartus II project and from there open SOPC builder.
Create a system according to the picture on next page
  You’ll find hpd’s tcl file from hpd’s vhd directory to add the component to the project
    Remember to set IP search path for it (tools->options)
  Use same names
  For this test set HIBI_PE_DMAs n_stream_chans_g to 0 and n_packet_chans_g to 8.
  Make instruction memories large enough for software
  Add reset ports to all CPUs
  Other components should work with default settings
  Use auto-assign for base addresses
  Disconnect unnecessary IRQ connections
Check create simulation files and generate

## Slide 8: NIOS II Eclipse
Create three “NIOS 2 Application and BSP template” projects named cpu0, cpu1 and cpu2
Copy all source/header files to all projects (from ../tb/system/src_cpu#)
Create BSP for all
  Rigth click -> nios II -> bsp editor -> generate
Compile all codes by selecting ”Build project” for each project

## Slide 9: Create initialization files for memories

## Slide 10: Modelsim simulation
Navigate your modelsim to the simulation folder it created earlier
Add hibi files to the compilation script
  Add to setup_sim.do the contents of msim_includes.txt (change paths!) (tb/system/support)
  Use hibiv3_r4 top level. Address ranges for cpus 0,1,2 are 0x000-0x1FF, 0x200-0x3FF, 0x400-0x5FF
    Tb/system/ contains one
  Add hibi to the simulation top level
    Locate vhd file named after you SOPC project
    Scroll to the bottom of it
    Modify it to be similar to tb/system/support/hibi_add.vhd
      Check DUT’s component name

## Slide 11: Modelsim simulation
In modelsim’s transcript window type ”do setup_sim.do” to setup things
S: compiles hw files
Jtag_*: commands to see what CPUs are printing in console windows, by default goes to transcript window
It takes about 1ms before CPUs start executing main() and simulations take a lot of time
Modify CPU1’s main.c to adjust the amount of packets that ping-pong between CPUs
They do not stop automatically!

## Slide 12: Next some examples how HPD should behave

## Slide 13: Enabling HPD to interrupt
// Enable interrupts on HPD side, set bit 1 high on register 4
IOWR(HIBI_PE_DMA_0_BASE, 4, (2 | (IORD(HIBI_PE_DMA_0_BASE,4))));
Read reg 4
Write back
With bit 1 high
Interrupts
on

## Slide 14: Channel rx configuration
Just four writes
// Set receive mem address for incoming data
IOWR(HIBI_PE_DMA_0_BASE, (rx_channel << 4), HPD_REGISTERS_RX_BUFFER_START + rx_addr);
// Set words to receive
IOWR(HIBI_PE_DMA_CHAN_0_BASE, (rx_channel << 4) + 2, rx_amount);
// Set hibi address to receive data
IOWR(HIBI_PE_DMA_0_BASE, (rx_channel << 4) + 1, hibi_addr);
// Initialize (enable) receiving
IOWR(HIBI_PE_DMA_0_BASE, 5 , 1 << rx_channel);

## Slide 15: TX
// Poll HPD, until it's not sending previous tx anymore
while(((IORD(HIBI_PE_DMA_1_BASE, 4) >> 16) & 0x1) == 0) { }
// Set data source address
IOWR(HIBI_PE_DMA_1_BASE, 8, data_src_addr);
// Set amount to send
IOWR(HIBI_PE_DMA_1_BASE, 9, amount);
// Set target hibi command
IOWR(HIBI_PE_DMA_1_BASE, 10, 2);
// Set target hibi address
IOWR(HIBI_PE_DMA_1_BASE, 11, hibi_addr);
// Start the transfer, set bit 0 high in register 4
IOWR(HIBI_PE_DMA_1_BASE, 4, (0x1 | (IORD(HIBI_PE_DMA_1_BASE,4))));
Data is written to hibi from shared memory

## Slide 16: Preconfigured transfer receive
Words are forwarded directly to shared memory until all words have been received
When all have been received interrupt is raised
Interrupt
Forward to shared mem directly
First packet
Second packet

## Slide 17: Unconfigured receive
IRQ has been raised quite many cycles ago
CPU reads the cause of IRQ
And the unknown
Incoming address
Ack IRQ
And later the same day (many many clock cycles):
CPU configures some channel for receiving to address 0x11 and N2H interrupts again when all data has been received