## Slide 1: Setting up udp-flood demo
Lauri Matilainen, Erno Salminen
TUT
April 2012

## Slide 2: Phases
Connect Altera DE2 FPGA board to PC using a cross-connected ethernet cable
Synthesize logic and program FPGA
  Controller for ethernet PHY chip
  Logic for handling UDP/IP headers and packets
  Simple flooder unit that just sends packet all the time
  Reset switch is
Capture the incoming UDP packets on Linux PC
  Using netstat -s
  Using netcat: nc –lup 5000
  Using test program udp_example.cc

## Slide 3: FPGA architecture
Run these

## Slide 4: Generated top-level vhdl
…
Flooder will send packets to this IP address 10.0.0.1 and port 5000
MAC address is not needed unless…

## Slide 5: Setup the IP address of PC
Put the same IP address here as in vhdl (prev slide)

## Slide 6: IP address of the DE2 board
DE2’s IP addr= 10.0.0.10

## Slide 7: DE2 board
Switch17 (pinV2) is the reset. Up-position means normal operation, down-position means reset
LEDG0 (PIN_AE22) lights up when link to PC has been established. This takes few seconds.
Use the mode ”RUN”
LEDR0 (PIN_AE23) turns on/off when a packet arrives from PC in receiver test.

## Slide 8: netcat
Make PC listen: nc –lup 5000
  You should see one ASCII char per line in increasing order
  Had to ask TSTWIN admin to change firewall settings for nc
  -l means listen
  - u UDP mode
  -p xxxx defines the port
Send PC -> FPGA(udp_Receiver_example_dm9000
  nc –uvv 10.0.0.10 6000
  Led changes state for each packet that is received in FPGA
  Each nc call just sends one packet (and gets stuck)
  Press Ctrl-c and try again. Led should be inverted

## Slide 9: netstat
Netstat -s
Look for category ”UDP statistics for ipv4”
”Datagrams received” tells the amount of data that PC recevied
  Should increase continuously with flood example

## Slide 10: Flood + netcat
First symbols
Running numbers
After a while it starts looking funny but no worries…

## Slide 11: Receiver example +Netstat + netcat
$netstat –s
…
… (part of mesasges hidden here)
Some data has been sent PC -> FPGA
Send one UDP packet PC -> FPGA, led changes its state
Cryptic looking error does no harm(?)
Sent data amount has increased

## Slide 12: Test program udp_example.cc
Send packets going to DE2 to this IP address 10.0.0.1
PC’s IP address 10.0.0.1
PC’s port 0x1388 = 5000
Does not do anything useful with flood example (2012-03-30, ES)
  Due to firewall settings???
Sends one packet = Invert the led on FPGA for each execution with receiver example. Note that most of code is not useful for receiver testing!
Send PC -> FPGA and nothing useful happens after print

## Slide 13: What all_waves.do looks like
1) Eth PHY is initialized
2)Some init phases take a long time
3)Phase 23 is the last. Link_wait_ime_c was shortened by 10000x in this sim
4)When eth phy is ready, flooder can start
4)When eth phy is ready, flooder can start. Cannot simulate further without an eth phy model, simple do-file cannot imitate it adequately

## Slide 14: Summary
Easy.